## Slide 1
Jie Hu, Li Shen, Samuel Albanie, Gang Sun, Enhua Wu
journal version of the CVPR 2018 paper
Paper Report
Squeeze-and-Excitation Networks

## Slide 2
01 Abstract
02 Introduction
03 Model and Computational Complexity
04 EXPERIMENTS
05 CONCLUSION
CONTENTS

## Slide 3
Abstract
In this work, we focus instead on the channel relationship and propose a novel architectural unit, which we term the “Squeeze-and-Excitation”(SE) block, that adaptively recalibrates channel-wise feature responses by explicitly modelling interdependencies between channels.

## Slide 4
Introduction
The Squeeze-and-Excitation(SE) block, with the goal of improving the quality of representations produced by a network by explicitly modelling the interdependencies between the channels of its convolutional features.

## Slide 5
Introduction
We propose a mechanism that allows the network to perform feature recalibration, through which it can learn to use global information to selectively emphasise informative features and suppress less useful ones.

## Slide 6
Introduction

## Slide 7
Introduction
Squeeze
經過Fsq找出channel中的global information，透過Global Average Pooling ，將原本shape為H*W*C的資料，轉換為1*1*C，意思是每個channel都變為一個值(channel descriptor)。

## Slide 8
Introduction
Global Average pooling(GAP)

## Slide 9
Introduction
使用GAP的原因
因為進行Convolution得到的輸出與前一層的每個channel都有複雜的關係，使用GAP簡化後，得到的每一點都只與一個channel有對應關係。

## Slide 10
Introduction
Excitation
透過Fex學習每個channel descriptor的重要程度，包含兩層全連接層。

## Slide 11
Introduction
Excitation
兩層全連接層，先降維再升維，以降低模型複雜度。

## Slide 12
Introduction

## Slide 13
Introduction
Instantiations

## Slide 14
Model and Computational Complexity
這部分會比較含有SE block的Model與原本Model的架構和複雜度（ResNet、SE-ResNet-50和SE-ResNeXt-50）。

## Slide 15
Model and Computational Complexity

## Slide 16
Model and Computational Complexity

## Slide 17
Model and Computational Complexity
模型加入SE block後，所增加的參數量為
r : reduction ratio
S : number of stages
Cs : dimension of the output channels
Ns : number of repeated blocks for stage s

## Slide 18
Model and Computational Complexity

## Slide 19
Experiments
In this section, we conduct experiments to investigate the effectiveness of SE blocks across a range of tasks, datasets and model architectures.

## Slide 20
Experiments
Network depth

## Slide 21
Experiments
Integration with modern architectures

## Slide 22
Experiments
Integration with modern architectures

## Slide 23
Ablation Study
Reduction ratio
測試SE Block中Excitation的全連接層降維多少效果會最好。

## Slide 24
Ablation Study
Squeeze Operator
比較使用Global Average Pooling和Global Maximum Pooling，發現GAP結果較好。
Excitation Operator
比較Excitation全連接層第二層的activation function使用ReLU、tanh和sigmoid，發現sigmoid最好，ReLU最差。

## Slide 25
Ablation Study
Different stages
比較在model不同的stage加入SE block，有什麼差別。

## Slide 26
Ablation Study
Effect of Squeeze
測試將Squeeze中的GAP層換成1 x 1 conv層並比較結果（代表不同channel還是會互相影響）。

## Slide 27
Conclusion
本篇論文提出的SENets，使用SE block這種新單元，用來加入其他現有的model，找出哪些channel擁有更重要的特徵，以達到更好的效果，並且只需要少量的計算，就能大幅提升model的表現。